## Slide 1: SHEQS Environmental Management Input
Stepdown CNC Minor Renovations and Repairs
06 May 2025

## Slide 2
Stepdown CNC
Watercourse/
Wetland
ISSUES IDENTIFIED:
Wall Paint Falling Off and Roof Collapsing after a short while due to molding.
FINDINGS:
Molding was identified (Walls and Roofs) during the inspection done 24 April 2025 at Stepdown CNC. ROOT CAUSE:
Stepdown CNC is situated in a wet area (see figure on the left). It is therefore prone to Moisture, Humidity, and Condensation that interacts with Material (Wood, Drywall, Walls, Windows, Pipes etc.) which results in mold thriving. Lack of proper Ventilation also encourages further mold growth.
TEAMS TO BE INVOLVED:
Dx Properties, Occupational Health & Safety, Environmental Management.
SUMMARY

## Slide 3
FINDINGS
These are some of the pictures taken from site showing mold that’s affecting the walls and roof.

## Slide 4
RESOLUTION
Immediate Short-term Long-term
Chemical Treatment
Contract mold treatment specialists to apply SABS approved mold treatment.
Expert Guidance
Consult a Damp/Waterproofing Specialist to test the area and make recommendations guided by the results.
Ventilation
Use airbricks/ louvre Vents for the walls. Use Ridge vents//Soffit vents/Turbine vents for the roof. Use Trickle vents for the windows.
Paint
Use moisture resistant paint such as PLASCON DAMPSEAL waterproofing paint.
Underground Drainage System
Invest in a drainage system manage ground water and improve integrity of the house foundation and walls. A gravel-based French drain system combined with surface drainage is best.
Concrete Apron
Install apron to help deviate surface water and protect foundation.
Cheaper alternative

## Slide 5
RESOLUTION (pictures)
Wall Air Brick
Roof Ridge vent
Wall Louvre vents
Roof Turbine vent
Roof Soffit vent
Window Trickle vent

## Slide 6
Recommended updates: Technical Requirements
Demonstrate Relevant Certification: Ensure that contractors are registered with DWASA (Damp and Waterproofing Association in Southern Africa), PRAWA (Professional Roof Repair and Waterproofing), WAG (Waterproofing Association of Gauteng) or any other relevant body that can confirm their expert knowledge in dealing with mold.
Demonstrate sufficient experience and knowledge: Submit work portfolio’s (photos and references) of previous jobs done in wet/damp environments and demonstrate knowledge on inspection and diagnosis skills.
Paints/Coating MSDS/Technical datasheet: Submit MSDS of paints/coating they use for waterproofing purposes with the aim of reducing mold buildup.
Guarantees/Warranties 3 to 5-year warranty for the waterproofing painting/coating work minimum.

## Slide 7
CONCLUSION
Stepdown will continuously have issues because it is unfortunately in the wetland and the building is old.
It’s also Important for the CNC to also do their best to practice good manual ventilation behavior:
    Open Windows daily (15-30 minutes), on opposite sides of the house (cross ventilation), and during humidity heavy activities that cause steam/moisture.
    Wipe moisture from surfaces (windows/walls/floors/surfaces).
Avoid blocking ventilation by removing furniture from the walls and keep interior doors open.
Invest in portable dehumidifier/Fans.

## Slide 8: Thank You